## Slide 1
Zhuoheng Li
2022.11
Use Reinforcement Learning to Generate Testing Commands for Onboard Software of Small Satellites

## Slide 2
Notice
This presentation is formular-free.
Chapter 4 in the thesis contains derivations.

## Slide 3
Notice
Sorry…
200+ slides, but I only discuss a small part of it today.

## Slide 4
Notice
Thesis and literature study documents available on Google Scholar with “onboard software testing” + “reinforcement learning” (the first result).
Slides and code are available on github.com/StarCycle
Full presentation has been uploaded to Youtube and Bilibili (under checking).

## Slide 5: Content
Overview
Background
Method
Experiments
Conclusions & Recommendations

## Slide 6: Content
Overview
Background
Method
Experiments
Conclusions & Recommendations
Interesting for the general space engineers

## Slide 7: Content
Overview
Background
Method
Experiments
Conclusions & Recommendations

## Slide 8
Overview
Main research question:
Can we use reinforcement learning (RL) to generate testing commands for small satellites with limited prior knowledge?

## Slide 9: Overview
What I try (part 1):
  3 RL algorithms (Q-Learning, D3QN, PPO)
  3 state representations (scalar generated by rules, branch coverage vector, graph)
  2 action spaces (Discrete, Multi-Discrete)
  3 neural network architectures (MLP, GGNN, GAT) + different pooling mechanisms
  2 ways to generate graph representation of source code (static analysis, dynamic analysis)
  2 testing goals (maximize code coverage or CPU load)

## Slide 10: Overview
What I try (part 2):
  2 environments (a toy problem and the COMMS software)
  2 testing senarios (normal testing and regression testing)
  2 baselines (random testing and the genetic algorithm)
  Generate testing commands on a local PC / cloud server
  Implement open-source tool to retrieve branch coverage from embedded software
  Other tools, like the command/response parser, state identification module, are developed in the study

## Slide 11
Overview
Very brief answer:
Yes, RL-based testing performs better under some conditions compared with the two baselines

## Slide 12: Content
Overview
Background
Method
Experiments
Conclusions & Recommendations

## Slide 13: Content
Overview
Background
Method
Experiments
Conclusions & Recommendations

## Slide 14
Background
About Delfi-PQ
Software Testing
Sequential Decision Making
RL-Based Testing

## Slide 15
Background
About Delfi-PQ
Software Testing
Sequential Decision Making
RL-Based Testing
Interesting for the general space engineers

## Slide 16
Background
About Delfi-PQ
Software Testing
Sequential Decision Making
RL-Based Testing

## Slide 17
Background / About Delfi-PQ
Delfi-PQ is an open-source, low-cost, tiny satellite series.
Launch a PQ periodically so we always have a PQ in lab for students and researchers.

## Slide 18
  First Delfi-PQ:
  3P PocketQube
  Size: 5*5*15cm
  Weight: ~0.5kg
  Power: average 1W
  Downlink speed: 150Byte/s~1.2KB/s
Background / About Delfi-PQ

## Slide 19
  Subsystems
  Power Lines (managed by EPS)
  Message Bus (managed by OBC)
  OBC: On-Board Computer
  EPS: Electrical Power System
  COMMS: Communication System
Background / About Delfi-PQ

## Slide 20
There are a microcontroller (MCU) and peripherals in each subsystem.
Software runs on the MCU to control the peripherals.
Background / About Delfi-PQ

## Slide 21
  Take COMMS as an example
  Power Lines (managed by EPS)
  Message Bus (managed by OBC)
  OBC: On-Board Computer
  EPS: Electrical Power System
  COMMS: Communication System
Background / About Delfi-PQ

## Slide 22
  Microcontroller
  Transceiver
  Receiver
  Power amplifier
  Low noise amplifier
  Downlink antenna
  Uplink antenna
  Satellite Bus (UART)
  Main Board
  Daughter Board
  Communication system (COMMS)
Background / About Delfi-PQ

## Slide 23
  COMMS Main Board
Broekhuizen, C. H., Speretta, S., Uludag, M. S., van den Bos, M., Haenen, J., Menicucci, A., & Gill, E. (2020). Miniaturized Radio Tranceiver for PocketQubes, Exceeding Performance of CubeSat Solutions.
  MSP432(ARM M4F)
Watchdog
Background / About Delfi-PQ

## Slide 24
Only the onboard computer (OBC) can send commands to subsystems.
Background / About Delfi-PQ

## Slide 25
OBC
COMMS
How are you?
(command to housekeeping service)
Background / About Delfi-PQ

## Slide 26
OBC
COMMS
My bit rate is
1200 bps
(Reply of housekeeping service)
Background / About Delfi-PQ

## Slide 27
OBC
COMMS
Set the rate to 9600 bps
(Command of radio service)
Background / About Delfi-PQ

## Slide 28
OBC
COMMS
Yes, I have done that
(Reply of radio service)
Background / About Delfi-PQ

## Slide 29
COMMS receives telecommands from the ground station, put the telecommands in a buffer, and wait for OBC to fetch these telecommands
Background / About Delfi-PQ

## Slide 30
OBC
COMMS
Telecommand
  Ground Station
Background / About Delfi-PQ

## Slide 31
OBC
COMMS
Do you receive any ground command?
(Command of radio service)
  Ground Station
Background / About Delfi-PQ

## Slide 32
OBC
COMMS
Yes, I send it to you
(Reply of radio service)
Telecommand
  Ground Station
Background / About Delfi-PQ

## Slide 33
OBC
COMMS
Oh, it’s a command for EPS. EPS should …
  Ground Station
EPS
Background / About Delfi-PQ

## Slide 34
OBC
COMMS
EPS
OK
  Ground Station
Background / About Delfi-PQ

## Slide 35
OBC
COMMS
EPS has done that. COMMS should send the reply to the ground
Reply of telecommand
  Ground Station
Background / About Delfi-PQ

## Slide 36
OBC
COMMS
Yes, I send it to the ground station
Reply of telecommand
  Ground Station
Background / About Delfi-PQ

## Slide 37
The command handler, as a special task, manages bus communication.
It has services to process received commands.
Background / About Delfi-PQ

## Slide 38
OBC
COMMS
Set the rate to 9600 bps
(Command of radio service)
Background / About Delfi-PQ

## Slide 39
Tasks of COMMS running on DelfiPQcore
Command handler
Radio task
Task A
Task B
Task …
Set the rate to 9600 bps
(Command of radio service)
Radio service
Service
2
Service
…
Let radio service to process it
Background / About Delfi-PQ

## Slide 40
Command handler
Radio task
Task A
Task B
Task …
Radio service
Service
2
Service
…
Let radio task to do something
Tasks of COMMS running on DelfiPQcore
Background / About Delfi-PQ

## Slide 41
Command handler
Radio task
Task A
Task B
Task …
Radio service
Service
2
Service
…
Get results from radio task
Tasks of COMMS running on DelfiPQcore
Background / About Delfi-PQ

## Slide 42
Tasks of COMMS running on DelfiPQcore
Command handler
Radio task
Task A
Task B
Task …
Hello OBC, I finished it
Radio service
Service
2
Service
…
Background / About Delfi-PQ

## Slide 43
The onboard software has different layers.
Background / About Delfi-PQ

## Slide 44
Hardware abstraction layer
DelfiPQcore
Tasks
Hardware driver libraries, provided by 3rd party (with our modifications)
Background / About Delfi-PQ

## Slide 45
Hardware abstraction layer
DelfiPQcore
Tasks
Real-time operation system (RTOS) made in house, because …
Background / About Delfi-PQ

## Slide 46
Hardware abstraction layer
DelfiPQcore
Tasks
Tasks are like applications on your phones.
Different subsystems have different tasks
Background / About Delfi-PQ

## Slide 47
Compare Delfi-PQ onboard software with other onboard software
Background / About Delfi-PQ

## Slide 48
Onboard Software Repository | Number of Lines of Code | Language
Delfi-PQ Flight Software | 20107 | C, C++
NASA Core Flight System | 100132 | C, C++, Python, Perl
NASA JPL F Prime | 82915 | C, C++, Python
KubOS | 57968 | Rust, C, Python
ESA Nanosat-MO-Framework | 543396 | Java
Cal Poly libproc for CubeSat | 25649 | C, C++
FossaSat-1 Pocosatellite | 1534 | C++
EASAT-2 PocketQube | 1816 | C
MelbourneSpaceProgram | 21668 | C, C++
Simpler than software for “big” satellites
Background / About Delfi-PQ

## Slide 49
Onboard Software Repository | Number of Lines of Code | Language
Delfi-PQ Flight Software | 20107 | C, C++
NASA Core Flight System | 100132 | C, C++, Python, Perl
NASA JPL F Prime | 82915 | C, C++, Python
KubOS | 57968 | Rust, C, Python
ESA Nanosat-MO-Framework | 543396 | Java
Cal Poly libproc for CubeSat | 25649 | C, C++
FossaSat-1 Pocosatellite | 1534 | C++
EASAT-2 PocketQube | 1816 | C
MelbourneSpaceProgram | 21668 | C, C++
Similar, or more complex than other CubeSat / PocketQube software
Background / About Delfi-PQ

## Slide 50
Delfi-PQ onboard software
NASA core Flight System (cFS)
They also have different layers
Background / About Delfi-PQ

## Slide 51
Application in cFS | Explanation | Similar Functionality in Delfi-PQ
Health and Safety App | Kick watchdog, monitor applications and events, take table-defined actions | Kick watchdogs, but do not monitor tasks and take recovery actions
Housekeeping App | Collects and re-packages telemetry from other applications | Housekeeping service
Data Storage App | Record housekeeping, engineering. and science data onboard for downlink | OBC state machine does it
File Manager App | Interfaces to the ground for managing files | No
Limit Checker App | Compare the telemetry with thresholds and take table-defined actions | OBC state machine checks some telemetry parameters
Memory Dwell App | Sample data at any process address | No
Scheduler App | Schedule onboard applications | DelfiPQcore scheduler can do it
Stored Command App | Executes preloaded command sequences at predetermined time | No. Delfi-PQ execute all ground commands immediately
Software Bus Network | Passes Software Bus messages over various “plug-in” network protocols | No. Delfi-PQ has some dirty ways for inter-task communication, such as call back functions and global viriables
Checksum APP | Performs data integrity checking of memory, tables, and files | Delfi-PQ will check MD5 of binary code during software update, but it won’t check that in normal operation
Memory Manager App | Provides the ability to load and dump memory | No
CFDP App | Transfers/receives file data to/from the ground according to CCSDS CFDF protocol | The telemetry service can transfer telemetry data from the SD card to the ground station. It doesn’t follow the CFDF protocol
Command Ingest Lab | Accepts CCSDS telecommand packets over a UDP/IP port | OBC state machine and the radio service accept ground commands. It doesn’t follow the CCSDS standard
Telemetry Output Lab | Sends CCSDS telemetry packets over a UDP/IP port | OBC state machine and the radio service send telemetry to the ground. It doesn’t follow the CCSDS standard.
Delfi-PQ tasks have similar functions as the mission-independent Apps in NASA cFS

## Slide 52
Application in cFS | Explanation | Similar Functionality in Delfi-PQ
Health and Safety App | Kick watchdog, monitor applications and events, take table-defined actions | Kick watchdogs, but do not monitor tasks and take recovery actions
Housekeeping App | Collects and re-packages telemetry from other applications | Housekeeping service
Data Storage App | Record housekeeping, engineering. and science data onboard for downlink | OBC state machine does it
File Manager App | Interfaces to the ground for managing files | No
Limit Checker App | Compare the telemetry with thresholds and take table-defined actions | OBC state machine checks some telemetry parameters
Memory Dwell App | Sample data at any process address | No
Scheduler App | Schedule onboard applications | DelfiPQcore scheduler can do it
Stored Command App | Executes preloaded command sequences at predetermined time | No. Delfi-PQ execute all ground commands immediately
Software Bus Network | Passes Software Bus messages over various “plug-in” network protocols | No. Delfi-PQ has some dirty ways for inter-task communication, such as call back functions and global viriables
Checksum APP | Performs data integrity checking of memory, tables, and files | Delfi-PQ will check MD5 of binary code during software update, but it won’t check that in normal operation
Memory Manager App | Provides the ability to load and dump memory | No
CFDP App | Transfers/receives file data to/from the ground according to CCSDS CFDF protocol | The telemetry service can transfer telemetry data from the SD card to the ground station. It doesn’t follow the CFDF protocol
Command Ingest Lab | Accepts CCSDS telecommand packets over a UDP/IP port | OBC state machine and the radio service accept ground commands. It doesn’t follow the CCSDS standard
Telemetry Output Lab | Sends CCSDS telemetry packets over a UDP/IP port | OBC state machine and the radio service send telemetry to the ground. It doesn’t follow the CCSDS standard.
But,
- Mission-dependent Apps in cFS are more complex
- We do not follow some standards, e.g., CCSDS CFDF

## Slide 53
  In the DelfiPQcore level:
  DelfiPQcore provides similar capabilities to core Flight Executive (cFE) of cFS.
  But it does NOT have a formal inter-task communication interface.
  It also does NOT have complex fault-handling mechanism.
Background / About Delfi-PQ

## Slide 54
Delfi-PQ was launched in January 2022.
It is working now.
Background / About Delfi-PQ

## Slide 55
Cape Canaveral
Background / About Delfi-PQ

## Slide 56
After launch
Background / About Delfi-PQ

## Slide 57
Background
Telemetry in past 30 days

## Slide 58
There were problems due to lack of testing…but we are lucky!
(More stories in the thesis document)
Background / About Delfi-PQ

## Slide 59
Background
About Delfi-PQ
Software Testing
Sequential Decision Making
RL-Based Testing

## Slide 60
Background
About Delfi-PQ
Software Testing
Sequential Decision Making
Reinforcement Learning

## Slide 61: Background / Software Testing
    Definitions
  Test case is a pre-written sequence of testing commands which will be executed during a test.
  By contrast, test command generation selects commands in real time, according to the current state (my study).
  Test oracle is a set of conditions to determine whether the system under test behaves correctly or not.
  Test coverage is a metric that shows the amount of testing performed. Different coverage types: code coverage (line, branch, MC/DC...), state coverage, requirement coverage, etc.

## Slide 62: Background / Software Testing
    Definitions
  Testing goals are immediate goals that help testers find bugs.
  Examples include:
  Maximize specific test coverage (code/state/requirement coverage)
  Maximize a computable metric (CPU load, estimated risk, etc)

## Slide 63: Background / Software Testing
    Definitions
  Regression testing tries to confirm a recent code change has not affected existing features.

## Slide 64
Write test cases manually takes too much human effort and prior knowledge from experts.
Background / Software Testing

## Slide 65
You are looking for a bug
Bug
And your prior knowledge may be wrong
Credit: Warner Bros.

## Slide 66
Background / Software Testing
    A serious software problem identified before launch
  Sometimes new software cannot be started after software update, so PQ is still using the old software.
  Software update is critical for PQ, since the team did not finish all onboard software before the launch.
  In fact, we found other serious problems in orbit, which could only be fixed by software update.

## Slide 67
Background / Software Testing
    So why couldn’t we identify it earlier?
  Output looked correct, except the software version MD5. Nobody checked the MD5 string.
  We assumed that errors located in the software update precedure. However, it occured after the procedure.
  The error only occured when several conditions were satisfied.

## Slide 68
Traditionally, how to reduce human effort and prior knowledge in software testing?
Background / Software Testing

## Slide 69
  Model-based test generation, e.g., human specify a finite state machine (FSM) of system under test and use a tool to traverse the FSM. The traversal paths are recorded as test cases.
  Symbolic execution substitutes all program variables with symbolic values, simulates execution of tested software step by step with constraint solving, and looks for all executable paths
  Random testing, i.e., select commands randomly.
  Search-based testing, use evolutionary algorithms (like the genetic algorithm) to modify a test cases written by human.
Background / Software Testing

## Slide 70
Background / Software Testing

## Slide 71
    Only search-based testing can deal with this situation:
  No model exists (our case)
  System-level testing (our case)
  Also achieve testing goals other than code coverage (helpful)
Background / Software Testing

## Slide 72
    But traditional search-based testing with evolutionary algorithms has shortages:
  Discard information observed at each test case step. Only use final objective function of the whole test case.
  Output a fixed solution, which may not work well in a non-deterministic environment.
  Cannot learn the pattern of a series of software. Testers need to re-run the time-consuming algorithm in regression testing.
Background / Software Testing

## Slide 73
How to solve these challenges?
You can look from a view of AI researchers.
Background / Software Testing

## Slide 74
Background
About Delfi-PQ
Software Testing
Sequential Decision Making
RL-Based Testing

## Slide 75
Background
About Delfi-PQ
Software Testing
Sequential Decision Making
RL-Based Testing

## Slide 76
Software testing is a sequential decision-making process.
Background / Sequential Decision-Making

## Slide 77
Background / Sequential Decision-Making
Strøm, M. A., Rehn, C. F., Pettersen, S. S., Erikstad, S. O., Asbjørnslett, B. E., & Brett, P. O. (2018). Combining design and strategy in offshore shipping. In Marine Design XIII (pp. 147-162). CRC Press.

## Slide 78
Background / Sequential Decision-Making
Depending on how knowledge is encoded:
- Symbolism encodes knowledge with symbols, which are interpretable.
- Connectionism encodes knowledge neural networks.
Depending on action space:
- Discrete. There are limited number of actions.
- MultiDiscrete. Select n discrete actions in a step.
- Continuous.

## Slide 79
Background / Sequential Decision-Making
Depending on underlying techniques:
- If the state/action space is small and discrete, a state machine is enough. Variants include procedures and petri nets,
- If the state/action space is large but discrete, you can try implicit graph search. Examples are classical planning and expert systems.
- If the state/action space is continuous, you may transfer it to an optimization problem, which can be solved by gradient descent, mathematical programing, evolutionary algorithms, etc.
- Sometimes you can directly calculate the action with formulars, like PID control.
- Learning is fitting an implicit function to calculate the result (supervised / unsupervised / reinforcement learning)

## Slide 80
Background / Sequential Decision-Making
If we look back at the test case generation methods:
- Model-based testing: state machine + graph search
- Symbolic execution: implicit graph search
- Random testing: no decision making
- Search-based testing with evolutionary algorithms: optimization

## Slide 81
Note that we widely use sequential decision-making techniques in space industry.
Background / Sequential Decision-Making

## Slide 82
Background / Sequential Decision-Making
Task Planning:
- Focus on “what to do”.
- It usually uses graph search techniques.
- 1st planner for space is DEVISER by NASA JPL for
the Voyager mission (early 1980s).
- 1st onboard planner is the PS module by NASA Ames
Center for the Deep Space-1 mission (1998).
- Recent mission: Perseverance Mars rover (ground
planner, NASA JPL, 2020), Amazônia-1 satellite (onboard
planner, Brazil, 2021)
Nau, D. S. (2007). Current trends in automated planning. AI magazine, 28(4), 43-43.

## Slide 83
Background / Sequential Decision-Making
State Machine:
- If the mission is simpler, you do not need complex task planning
State machine in Delfi-PQ OBC
(credit: Silvana Radu)

## Slide 84
Background / Sequential Decision-Making
Control:
- Low-level actions. Calculate with formulars/optimization.
Nau, D. S. (2007). Current trends in automated planning. AI magazine, 28(4), 43-43.
Free-floating arm control
(credit: Tether Unlimit)
Attitude control
(credit: Jian Guo)

## Slide 85
Background / Sequential Decision-Making
Scheduling:
- Focus on “when to do”.
- Schedule observation/communication.
- Transfer it to an optimization problem.
- A famous scheduler is SPIKE for the
Hubble Space Telescope (1990) and James
Webb Telescope (2021), developed by
STScI.
Weerdt, M. de (2021). What have satellite scheduling, the selected traveling salesperson problem, and make-to-order manufacturing in common? MultiParty Planning and Optimization.

## Slide 86
Background / Sequential Decision-Making
Two representative learning techniques for sequential decision-making in space are reinforcement learning and imitation learning
locomotion robot
(credit: ETH & ESA)
Robot arm manipulation
(credit: Surrey space center)
Multi-agent observation scheduling
(credit: NSSC & Tencent)
Izzo, D., Märtens, M., & Pan, B. (2019). A survey on artificial intelligence trends in spacecraft guidance dynamics and control. Astrodynamics, 3(4), 287-299.

## Slide 87
Use RL in onboard software testing on the ground?
Safe & Cheap,
Good computing power/tool chain,
Collecting millions of samples is OK,
Clear reward definition
Background / Sequential Decision-Making

## Slide 88
Background
About Delfi-PQ
Software Testing
Sequential Decision Making
RL-Based Testing

## Slide 89
Background
About Delfi-PQ
Software Testing
Sequential Decision Making
RL-Based Testing

## Slide 90
    Most of Reinforcement learning (RL) algorithms are developed for Markov Decision Process (MDP), which is a 4-tuple , where (Howard, 1960):
- is a set of states.
- is a set of actions.
- is the probability that action in state will lead to state .
- is the reward received after state transition.
Background / RL-Based Testing

## Slide 91
    MDP satisfies the Markov property, i.e., the state transition probability is only related to the current state and action , instead of the entire history.
    Some MDP also assumes the current state is fully observable.
Background / RL-Based Testing

## Slide 92
    In an MDP step, RL does the following things:
    1. Observe the environment
    2. Select an action according to the estimated policy function, value function, or environment model.
    3. Receive a reward (scalar).
    4. Update the approximators of policy function, value function, or environment model.
Background / RL-Based Testing
Credit: Technik und Wissen

## Slide 93
Background / RL-Based Testing
Depending on what to approximate, RL can be classified as:
- Value-based RL only learns the values of state-action pairs Examples include Q-Learning, DQN.
- Policy-based RL only learns the policy function 𝜋(𝑎|𝑠), i.e., the probability to choose action 𝑎 under state 𝑠. Example: REINFORCE.
- Actor-critic RL learns both and 𝜋(𝑎|𝑠). Examples are DDPG, A3C/A2C, PPO, TD3, and SAC.
- Model-based RL also learns an environmental model , which predicts future states and rewards. Examples are the World Model and Muzero.
- Note: learning a state machine is a heavily researched topic in computer science.

## Slide 94
    RL-Based Testing
    - At any testing level
    - Accept computable testing goals
    - A model is unnecessary
    - Use observation
    - Learn a policy, which can be used in non-derterministic environments
    - May learn the pattern in a series of software
    It’s real-time testing command geneation.
Background / RL-Based Testing
  - No model exists (our case)
  - System-level testing (our case)
  - Achieve different testing goals (helpful)
  - Fully utilize observation at each step (helpful)
  - Adapt to non-deterministic environment (helpful)
  - Work in regression testing (helpful)
    Traditional Methods does NOT satisfy our requirements

## Slide 95
    One of the benifits: use RL in regression testing
Train the agent in sprint 1
Run the agent in sprint 2, and train it at the same time
Background / RL-Based Testing

## Slide 96
    RL-based testing in getting popular in other fields, but not space industry and embedded SW testing yet...
  Bytedance, the company of TikTok, runs their RL agent Fastbot >10000 times per day, find >50000 crashes per month (2021).
  Electronic Arts, who made Need For Speed and Call of Duty, now use RL to test first-person shooter games (Bergdahl, 2020).
  Commercial RL-based testing tool providers: Test.AI (mobile app GUI testing, 2021), Diffblue cover (unit testing for Java, 2021), etc.
Background / RL-Based Testing

## Slide 97
    Comprehensive review of previous RL-based SW testing studies in section 2.3
Background / RL-Based Testing

## Slide 98
    Comprehensive review of previous RL-based SW testing studies in section 2.3
Background / RL-Based Testing
Research started from 2005.
Application started from 2019.

## Slide 99: Background / RL-Based Testing
    Why not use RL to test embedded SW / onboard SW?
  Space industry is a little conservative…
  Difficult to extract current state:
  - Embedded SW doesn’t have GUI.
  - The telemetry is not a complete description of state. For PQ, it only shows the satellite is healthy or not.
  - RL with partial observation is more complex.
  Difficult to define actions:
  - You need to keep the spacecraft (SC) safe.
  - SC has multiple inputs (commands, sensor readings, radio…)

## Slide 100: Background / RL-Based Testing
    Why not use RL to test embedded SW / onboard SW?
  Difficult to define rewards:
  - State coverage is hard, since you don’t know the current state
  - Interface coverage, i.e., collecting every type of replies, may not be sufficient
  - Requirement coverage needs prior knowledge
  Difficult to perform multi-system testing:
  - You have host PC, subsystem A/B/C on the same bus
  - Limited communication, compared with test SW on the same computer

## Slide 101
First one in this field.
Difficult life.
Background / RL-Based Testing

## Slide 102: Content
Overview
Background
Method
Experiments
Conclusions & Recommendations

## Slide 103: Content
Overview
Background
Method
Experiments
Conclusions & Recommendations

## Slide 104: Method
Last command
Current reply
Automatically collected information, e.g., code coverage
Last human-defined state (scalar)
Current human-defined state (scalar)
Human specified rules
RL algorithm
Action
(next command)
Receive reward
Function approximators
Embedding
(vector / graph)
[0, 1, …0]
With support from low-level hardware/software

## Slide 105: Method
Last command
Current reply
Automatically collected information, e.g., code coverage
Last human-defined state (scalar)
Current human-defined state (scalar)
Human specified rules
RL algorithm
Action
(next command)
Receive reward
Function approximators
Embedding
(vector / graph)
[0, 1, …0]
With support from low-level hardware/software

## Slide 106: Method/low-level hardware

## Slide 107: Method/low-level hardware
It can do single/multiple subsystem testing.
But I only test COMMS in the study.

## Slide 108: Method / low-level software
    Software layout

## Slide 109: Method
Last command
Current reply
Automatically collected information, e.g., code coverage
Last human-defined state (scalar)
Current human-defined state (scalar)
Human specified rules
RL algorithm
Action
(next command)
Receive reward
Function approximators
Embedding
(vector / graph)
[0, 1, …0]
With support from low-level hardware/software

## Slide 110: Method
Last command
Current reply
Automatically collected information, e.g., code coverage
Last human-defined state (scalar)
Current human-defined state (scalar)
Human specified rules
RL algorithm
Action
(next command)
Receive reward
Function approximators
Embedding
(vector / graph)
[0, 1, …0]
With support from low-level hardware/software

## Slide 111: Method / action
    Actions in Discrete action space:
  Human define the format, order, and values of command parameters in a csv file.
  IO processing module generates a command list.
  RL agent select a command from the list.

## Slide 112: Method / action
    Actions in MultiDiscrete action space:
  Human define possible parameter values in a csv file.
  RL agent select the values to form a command vector, whose length is set by human.
  [data 1, data 2, data 3, …, data N]
  Parameter list

## Slide 113
Discrete: safer
MultiDiscrete: less prior knowledge
Method / action

## Slide 114: Method
Last command
Current reply
Automatically collected information, e.g., code coverage
Last human-defined state (scalar)
Current human-defined state (scalar)
Human specified rules
RL algorithm
Action
(next command)
Receive reward
Function approximators
Embedding
(vector / graph)
[0, 1, …0]
With support from low-level hardware/software

## Slide 115: Method
Last command
Current reply
Automatically collected information, e.g., code coverage
Last human-defined state (scalar)
Current human-defined state (scalar)
Human specified rules
RL algorithm
Action
(next command)
Receive reward
Function approximators
Embedding
(vector / graph)
[0, 1, …0]
With support from low-level hardware/software

## Slide 116: Method / reward
    Possible rewards:
  State coverage
  Requirement coverage
  Risk
  Code coverage
  CPU loads
  …

## Slide 117: Method / reward
    Possible rewards:
  State coverage
  Requirement coverage
  Risk
  Code coverage
  CPU loads
  …
Significant prior knowledge
Difficulty to define risk
Computable

## Slide 118: Method / reward
    Reward 1: branch coverage growth after sending a command
  Commercial coverage measurement tools:
              - Cannot support all MCUs, especially TI MSP432 (e.g., Segger J-Trace)
              - Need external hardware (e.g., LDRA cover)
              - Expensive (Tessy €8000, LDRA cover €12000, VectorCAST €15000, …)

## Slide 119
Thus, make our own tool.
Method / reward

## Slide 120: Method / reward

## Slide 121: Method / reward

## Slide 122: Method / reward
    Reward 1: branch coverage growth after sending a command
  Coverage tool made in house (github.com/StarCycle/CodeCoverage)
  - Insert CodeCount() function in every branch, using regression expressions.
  - Low memory footprint
  Each CodeCount result is stored in 1 bit.
  COMMS: 716 CodeCounts, 90 byte
  OBC: 1329 CodeCounts, 167 byte
  Max payload size: 253 byte

## Slide 123
    Reward 1: branch coverage growth after sending a command:
    Coverage tool made in house (github.com/StarCycle/CodeCoverage)
  - Quick data transmission -> can do near real-time measurement
Method / reward

## Slide 124: Method / reward
    Reward 1: branch coverage growth after sending a command
    Coverage tool made in house (github.com/StarCycle/CodeCoverage)
  - Coverage report:

## Slide 125: Method / reward
  Theoretically, the tool can measure near real-time code coverage from any programming language, any MCU, and via any bus.
  It still has problems:
  1. Only support branch coverage
  2. Not very accurate because it uses regrex to parse the code
  3. Hitting CodeCount() takes time!
  But now it’s sufficient to calculate rewards. And these can be improved.

## Slide 126: Method / reward
    Reward 2: Estimated CPU load
  Estimate number of clock cycles required by each loop in the scheduler
the clock frequency of the CPU
the time interval being sampled
the number of loops executed by the scheduler during the time interval

## Slide 127: Method / reward
    Reward 2: Estimated CPU load

## Slide 128: Method / reward
    Reward 2: Estimated CPU load
Make CPU load uncertain

## Slide 129: Method
Last command
Current reply
Automatically collected information, e.g., code coverage
Last human-defined state (scalar)
Current human-defined state (scalar)
Human specified rules
RL algorithm
Action
(next command)
Receive reward
Function approximators
Embedding
(vector / graph)
[0, 1, …0]
With support from low-level hardware/software

## Slide 130: Method
Last command
Current reply
Automatically collected information, e.g., code coverage
Last human-defined state (scalar)
Current human-defined state (scalar)
Human specified rules
RL algorithm
Action
(next command)
Receive reward
Function approximators
Embedding
(vector / graph)
[0, 1, …0]
With support from low-level hardware/software

## Slide 131: Method / human-specified state
    Housekeeping telemetry is not enough to derive system state:
  What can you get from housekeeping telemetry?
Useless fields
They will NOT even change during a test

## Slide 132: Method / human-specified state
    You need more information to derive system state:
  Which command has been executed and their replies show current state of the system.
Command Definition
Reply Definition
if (last_state == xxx
&& command == xxx
&& reply == xxx):
current_state=xxx
State Extraction by rules

## Slide 133: Method / human-specified state
More complex than I expected at the beginning…but it’s engineering.
Can reuse it in other PQ software.

## Slide 134
Human-specified states use too much prior knowledge.
Method / human-specified state

## Slide 135: Method
Last command
Current reply
Automatically collected information, e.g., code coverage
Last human-defined state (scalar)
Current human-defined state (scalar)
Human specified rules
RL algorithm
Action
(next command)
Receive reward
Function approximators
Embedding
(vector / graph)
[0, 1, …0]
With support from low-level hardware/software

## Slide 136: Method
Last command
Current reply
Automatically collected information, e.g., code coverage
Last human-defined state (scalar)
Current human-defined state (scalar)
Human specified rules
RL algorithm
Action
(next command)
Receive reward
Function approximators
Embedding
(vector / graph)
[0, 1, …0]
With support from low-level hardware/software

## Slide 137: Method / automatic embedding of state

## Slide 138: Method / automatic embedding of state
Robust and straightforward, but…

## Slide 139: Method / automatic embedding of state
NOT suitable for regression testing

## Slide 140: Method / automatic embedding of state
Input is too long. Difficult to train.

## Slide 141: Method / automatic embedding of state
  So, I choose graph
CodeCount(1)
CodeCount(2)
CodeCount(3)
CodeCount(4)
Each node contains
- Information of this branch
- Whether the branch is covered
Directed edges have no weights

## Slide 142: Method / automatic embedding of state
  How to build this graph?
  You can use coverage measurement
  Embedded SW updates the following array:
  And host PC samples the array periodically
121 | 122 | 123
122 | 123 | 124
LastCodeCount
index
value
CodeCount(121)
CodeCount(122)
CodeCount(123)
CodeCount(124)
...

## Slide 143: Method / automatic embedding of state
CodeCount(121)
CodeCount(122)
CodeCount(123)
CodeCount(124)
122 | 123 | 124
121 | 122 | 123
When the current CodeCount is 124, the previous CodeCount is 123
index
value
...
Periodically sample the array and add edges to the graph

## Slide 144: Method / automatic embedding of state
    Result:
  Use coverage measurement to build control flow graph
  COMMS has 716 CodeCounts
  This method extracts 299, others not executed
  For GNN, the graph structure is changing.
  More communication load!
  No information of a branch.

## Slide 145: Method / automatic embedding of state
  So, build this graph with static code analysis
  TI Code Composer Studio can generate call graph, where each node is a function. However,
  - There are too many functions from low-level libraries
  - Cannot include a CodeCount() node
  - Tool-dependent, and I cannot modify the tool
  Other tools like CodeViz, rely on output from compilers like GCC and Clang. Unfortunately, they don’t support the old TI compiler we use

## Slide 146
But there is an open-source tool for code analysis research.
Method / automatic embedding of state

## Slide 147: Method / automatic embedding of state
  A parser for research: Joern
  - Parse C, C++, Java, Python, Bytecode, Kotlin, PHP…
  - Parse source code even if you cannot compile it
  - Flexible API
  - Mainly built for code vulnerability scanning
  Problems of Joern:
  - Weak to find calling relations among methods
  - The results contain errors

## Slide 148: Method / automatic embedding of state
    To use output of Joern:
  To find calling relations, writing my own code with Joern API
  Connect to all method with the same name
  Not accurate, but each program will have a static and unique graph structure, which is enough for GNN to recognize each node.
Method call, Console::log()
Method, Console::log(char *test)
Method, Console::log(void)
Method, XXX::log()

## Slide 149: Method / automatic embedding of state
    To use output of Joern:
  To find information of branches, use Word2Vec
  Word2Vec is a basic natural language processing algorithm to turn a string to a vector.
  First train Word2Vec with all source code.
  For each branch, convert the method name and file name to vector.
  Node vector is:

## Slide 150: Method / automatic embedding of state
    Result:
  Control flow graph from static code analysis
  1517 nodes, 3925 edges for COMMS
  3 types of node: CodeCount, Method,
  and MethodReturn
  Still incomplete because of parsing
  errors of Joern

## Slide 151: Method
Last command
Current reply
Automatically collected information, e.g., code coverage
Last human-defined state (scalar)
Current human-defined state (scalar)
Human specified rules
RL algorithm
Action
(next command)
Receive reward
Function approximators
Embedding
(vector / graph)
[0, 1, …0]
With support from low-level hardware/software

## Slide 152: Method
Last command
Current reply
Automatically collected information, e.g., code coverage
Last human-defined state (scalar)
Current human-defined state (scalar)
Human specified rules
RL algorithm
Action
(next command)
Receive reward
Function approximators
Embedding
(vector / graph)
[0, 1, …0]
With support from low-level hardware/software

## Slide 153: Method / RL algorithm
    This study tries three RL algorithms:
  Q-Learning
  D3QN: Dueling Double Deep Q Network
  PPO: Proximal Policy Optimization
  They are the most popular and robust RL algorithms
  Note: Each algorithm may have several configurations

## Slide 154: Method / RL algorithm
    Q-Learning
  Value-based RL, i.e., fitting the values of state-action pairs
  The approximator is a Q table.
  A state in Q-Learning must be a scalar.
  Thus, the scalar is extracted by rules, as mentioned before.
  An action must be a scalar, too.
  Thus, it only works in Discrete action space.

## Slide 155: Method / RL algorithm
    D3QN
  Value-based RL, i.e., fitting the values of state-action pairs
  Variant of Q-Learning, use a neural network as the approximator.
  State input can be a scalar, vector, or graph.
  Actions should be Discrete, otherwise
[17, 1, …2]
Length of the command vector is L, the number of available values is V, then the network should predict for times

## Slide 156: Method / RL algorithm
    PPO
  Actor-critic RL, i.e., fitting and 𝜋(𝑎|𝑠).
  May crash when policy update (estimated by KL divergence) is too quick.
  I add an annealing mechanism, i.e., if KL divergence is too high, reduce the learning rate.
  State input can be a scalar, vector, or graph.
  Actions should be Discrete or MultiDiscrete.

## Slide 157: Method
Last command
Current reply
Automatically collected information, e.g., code coverage
Last human-defined state (scalar)
Current human-defined state (scalar)
Human specified rules
RL algorithm
Action
(next command)
Receive reward
Function approximators
Embedding
(vector / graph)
[0, 1, …0]
With support from low-level hardware/software

## Slide 158: Method
Last command
Current reply
Automatically collected information, e.g., code coverage
Last human-defined state (scalar)
Current human-defined state (scalar)
Human specified rules
RL algorithm
Action
(next command)
Receive reward
Function approximators
Embedding
(vector / graph)
[0, 1, …0]
With support from low-level hardware/software

## Slide 159: Method / Function Approximator
    Neural Network Architecture
  If input is a vector, then just use 2~3 layers of MLP (fully connected layer)
The input vector is a concatenation of 2 vectors:
The code coverage vector
(In Discrete action space) A vector containing actions in previous k steps.
Output or 𝜋(𝑎|𝑠)

## Slide 160: Method / Function Approximator
    Neural Network Architecture
  If input is a graph, you need a graph neural network before the MLP
Graph with node features and edges. Code coverage is concatenated with node feature.
GNN
GNN updates node features.
Graph pooling layer extract a graph embedding vector from node features.
MLP
A vector containing actions in previous k steps (optional)

## Slide 161: Method / Function Approximator
    GNN
Hamilton, W. L., Ying, R., & Leskovec, J. (2017). Representation learning on graphs: Methods and applications. arXiv preprint arXiv:1709.05584.

## Slide 162: Method / Function Approximator
    GNN
  This study tries 2 types of GNN: Gated Graph Neural Network (GGNN) and Graph Attention Network (GAT)
  They appear in RL-based testing literature
  GGNN uses a gated recurrent unit (GRU) to aggregate node features
  GAT uses masked self-attention to aggregate node features (usually multi-head attention)

## Slide 163: Method / Function Approximator
    Graph Pooling Layer
  This study tries many graph pooling mechanisms, but the following two are most useful.
  Attentive pooling layer (for graph classification) in (Li, 2015).
  Use an MLP to reduce node embeddings to scalars and then concatenate these scalars into a vector. I call it feature compression.

## Slide 164: Method
    Algorithm Configurations:
    [RL algorithm] – [Action Space] – [Approximator]
  Q-Learning
  D3QN-Discrete-MLP
  D3QN-Discrete-GGNN
  D3QN-Discrete-GAT
  PPO-Discrete-MLP
  PPO-MultiDiscrete-MLP
  PPO-Discrete-GGNN
  PPO-Discrete-GAT
  PPO-MultiDiscrete-GGNN

## Slide 165: Method
    The implementation is lightweight. It mainly uses PyTorch and PyTorch Geometry. Some RL algorithms are modified from ClearRL, a single-file RL repository.
Configuration | File Name | Number of Lines of Code
PPO-MultiDiscrete-GGNN | PPO.py | 166
 | GNN_Agent.py | 124
Shared functions | PQ9Client.py | 81
 | MyEnv.py | ~100
 | PQ9cov.py | 153
 | GraphExtract.py | 143
 | MyWord2Vec.py | 20

## Slide 166: Method
    Two Baselines
  Random testing (Discrete, MultiDiscrete)
  Genetic Algorithm (Discrete, MultiDiscrete)

## Slide 167: Content
Overview
Background
Method
Experiments
Conclusions & Recommendations

## Slide 168: Content
Overview
Background
Method
Experiments
Conclusions & Recommendations

## Slide 169: Content
“Filling Grid” Test
Coverage Testing
Stress Testing
Regression Testing

## Slide 170: Content
“Filling Grid” Test
Coverage Testing
Stress Testing
Regression Testing

## Slide 171: Experiments / Filling Grid Test
First debug RL in a super simple environment

## Slide 172: Experiments / Filling Grid Test
Example: successful training process of D3QN

## Slide 173: Experiments / Filling Grid Test
Example: successful training process of PPO

## Slide 174: Experiments / Filling Grid Test
Example: successful training process of PPO

## Slide 175: Experiments / Filling Grid Test
Example: crashes of PPO without learning rate annealing

## Slide 176: Experiments / Filling Grid Test
  Findings about RL algorithms
  Convergence speed: D3QN>PPO (just in this test).
  Learning rate annealing avoids PPO from crashing. It also makes the final entropy higher but does not affect performance.
  Findings about Neural Networks
  Convergence speed: MLP>GGNN≈GAT, feature compression>attentive pooling
  Performance: GGNN>=GAT
  Stability: attentive pooling>feature compression

## Slide 177: Content
“Filling Grid” Test
Coverage Testing
Stress Testing
Regression Testing

## Slide 178: Content
“Filling Grid” Test
Coverage Testing
Stress Testing
Regression Testing

## Slide 179: Experiments / Coverage Testing
  Maximize branch coverage of COMMS software
  Reward +1 when cover new branch, otherwise -1
  The uncertainty is smaller than stress testing

## Slide 180: Experiments / Coverage Testing
  Findings
  Random testing will finally reach the branch coverage up limit in 30 minutes.
  Genetic algorithm finds optimal command sequence in an hour.
  PPO-Discrete-MLP reaches similar performance as the genetic algorithm after 3 hours.
  Other RL algorithms do not work or are unstable

## Slide 181: Content
“Filling Grid” Test
Coverage Testing
Stress Testing
Regression Testing

## Slide 182: Content
“Filling Grid” Test
Coverage Testing
Stress Testing
Regression Testing

## Slide 183: Experiments / Stress Testing
  Maximize estimated CPU load of COMMS software
  Non-deterministic,
  with unpredictable peaks
Sending the same command repeatedly

## Slide 184: Experiments / Stress Testing
  Genetic algorithm does not work very well because…
Genetic-Discrete

## Slide 185: Experiments / Stress Testing
  But RL performs well in such environment
PPO-MultiDiscrete-GGNN

## Slide 186: Experiments / Stress Test
  Findings about algorithms
  Random testing does not work.
  A fixed solution from the genetic algorithm is not suitable for such non-deterministic environment.
  Q-Learning does not converge.
  D3QN does not converge.
  All PPO algorithms converge.
  CPU load is much higher when the algorithm works within MultiDiscrete (for both genetic and PPO), if command vector length is not too long.
  CPU load has smaller variance when the algorithm works within MultiDiscrete (for both genetic and PPO).

## Slide 187: Experiments / Stress Test
  Findings about neural networks
  GGNN brings higher CPU load.
  GGNN also makes the variance higher.
  Convergence speed: attentive pooling>feature compression (different from filling grid test)
  Triggered CPU load: attentive pooling>feature compression

## Slide 188: Experiments / Stress Test
  Findings about performance
  Contrary to the traditional impression, PPO converges much more quickly than the genetic algorithm.
  It’s OK to run PPO on the lab PC in stress testing.

## Slide 189: Content
“Filling Grid” Test
Coverage Testing
Stress Testing
Regression Testing

## Slide 190: Content
“Filling Grid” Test
Coverage Testing
Stress Testing
Regression Testing

## Slide 191: Experiments / Regression Testing
  Train on a software version and test another version.
  Use PPO-MultiDiscrete-GGNN to perform stress testing.

## Slide 192: Experiments / Regression Testing
Genetic-MultiDiscrete

## Slide 193: Experiments / Regression Testing
PPO-MultiDiscrete-GGNN

## Slide 194: Experiments / Regression testing
  Findings
  PPO-MultiDiscrete-GGNN configuration does work in regression testing
  Performance of the trained agent remains the same.
  The trained agent and the agent trained from scratch have the same performance in the end.
  But the entropy of the trained agent is smaller.
  Reusing a fixed solution of the genetic algorithm does not have the same effect

## Slide 195: Experiments
  Bugs identified during these experiments
  Three bugs and one anomaly.
  But I did not define any testing oracles.
  Why?
  - Some faults are too obvious, e.g., crash, missing messages
  - If the tested software generates unexpected response, my parser cannot parse it.

## Slide 196: Content
Overview
Background
Method
Experiments
Conclusions & Recommendations

## Slide 197: Content
Overview
Background
Method
Experiments
Conclusions & Recommendations

## Slide 198: Conclusions & Recommendations
Brief answer: Yes, RL-based testing performs better under following conditions compared with the two baselines (part 1):
  Test in a non-deterministic environment, e.g., CPU load triggered by the same command is quite uncertain
  Use the PPO algorithm
  Encode code coverage in state, instead of rule-based features
  For Multi-Discrete action space, the command vector should not be too long
  PPO still has some benefits in Discrete action space

## Slide 199: Conclusions & Recommendations
Brief answer: Yes, RL-based testing performs better under following conditions compared with the two baselines (part 2):
  If you want regression testing, use GGNN with an attentive pooling layer in PPO
  Otherwise, 2~3 layers of MLP are enough
  Note: I cannot explain some phenomenons in the experiments, but they do not threaten the validity of the main conclusions

## Slide 200: Conclusions & Recommendations
Recommendations:
  Improve sampling efficiency, e.g., model-based RL
  Learn a model of the satellite in testing, and use the model in other fields, e.g., fault detection in spacecraft operation
  Simulate sensors and actuators in testing
  Try more RL-based regression testing. You may need to solve the generalization challenge of RL via multi-task learning, meta learning, etc.

## Slide 201: Feel free to drop me a message via zhuohengli@foxmail.com